## Slide 1: E+ Co-Simulation in Simulink
Zhelun Chen
08/20/2020

## Slide 2: Outline
Installation of EnergyPlusToFMU
Running E+ FMU in Simulink
Setup interface in E+

## Slide 3: Installation of EnergyPlusToFMU
Search for EnergyPlusToFMU, follow the installation guide https://simulationresearch.lbl.gov/fmu/EnergyPlus/export/userGuide/download.html
Some issues you may encounter during installation
  Make sure you change the directory for Visual Studio for all batch files in the script folder.
  If you cannot generate the .fmu file, it is probably because some folders cannot be removed. If so, disable the following code in the utilManageCompileLink.py
download
mine

## Slide 4: Running E+ FMU in Simulink
Use the example .idf files in the example folder
Create your FMU file, follow the instruction: https://simulationresearch.lbl.gov/fmu/EnergyPlus/export/userGuide/build.html
Or you can write a batch file to easily run python
Load .fmu into Simulink using a FMU block
Set stop time to be at least 86400 seconds
Double-click FMU block, set communication step size to be the same as in E+. For example, E+ uses 6 steps per hour, the step size is 600 seconds
Python script location
.idd location
.epw location
.idf location

## Slide 5: Running E+ FMU in Simulink
Before running, make sure E+’s path has been included in the computer environment

## Slide 6: Setup interface in E+
How to setup your own .idf file for FMU co-simulation
output
input

## Slide 7: Setup interface in E+
Properly define outputs
  Only variables included in Output:Variable can be export
  Check output file for the Key Name
  Variable Name can be selected after running the E+ model one time with Output:VariableDictionary turn on
Key Name
export
check output file
Variable Name
You name it

## Slide 8: Setup interface in E+
Simple interaction
  To:Schedule
High-Level interaction
  To:Actuator or To:Variable
    Works with EMS
    Allow you to change a lot of things. For example, you can override the supply air conditions.
  Read E+ EMSApplicationGuide.pdf for details

## Slide 9: Setup interface in E+
Before converting to FMU, check the .idf with text editor
  After editing with idf editor, Version and Version# may appear in different lines
  Make sure Version and Version# are in the same line